FreeWPC System Architecture
Machine Logic (Rules)
Common Logic
Device
Drivers
Hardware APIs
Task APIs
Operating
System
Scheduler
Hardware
Manager
Layer
Switch
Manager
Lamp
Manager
Solenoid
Managers
Display
Manager
Hardware Interface Layer (pinio)
Hardware Definitions

---
Portability Goals
Common code across all WPC generations (WPC, WPC-DCS, WPC-S, WPC-95)
Future support for other pinball platforms (e.g. Whitestar)
Future support for new pinball hardware designs
Native compilation on PC for easier debugging

---
Task Scheduler
Create new task
Query task still running
End current task
Stop different task

---
Hardware Interface Layer
Defines how the CPU accesses the hardware
Maps simple pinball I/O operations to the correct registers, access method
Examples:
  - Set switch matrix column (N)
  - Read current switch row
  - Turn on/off solenoid (N)
Numbering of devices is machine-specific!
May require tweaking as more architectures are supported

---
Hardware Managers
Common code that uses the Hardware Interface Layer to manage devices:
  - Duty cycling of coils
  - Strobing through the switch/lamp matrix
  - Debouncing inputs
  - Real-time error detection
Each manager provides two things:
  - A real-time function that accesses the hardware
  - APIs to higher layer software
    - Example: Read Switch #N

---
WPC Hardware Managers
Switch Manager
Lamp Manager
Power Driver Managers (Continuous & Duty-Cycled, used for solenoids, motors, and flashers)
Triac Manager (Lighting & Misc. Relays)
Display (DMD) Manager
Sound Board Manager

---
Device Drivers
Works in conjunction with hardware managers for specific types of devices (e.g. ejects, slingshots, kickbacks)
Can include real-time (IRQ-level) and ordinary (task-level) functions
A single driver can refer to multiple types of hardware (e.g. a slingshot driver utilizes a coil and a switch)
Mostly written as common code that is parameterized, similar to C++ templates.

---
Common Logic
A 'library' of functions common to all pinball games
Not tied to the hardware per se
Examples:
  - Pricing, DMD drawing, Flipper Codes, Replay system, Test mode, Game state machine, Display/Lamp/Sound Effect Choreography, Enter Initials, etc.

---
Machine Logic
Machine-specific functions for rules, effects, diagnostics, etc.
Also highly modular
Mostly event-driven, written as a series of callback functions to be invoked when certain things happen

---
Hardware Description
Mostly a set of tables that describe what hardware is connected to each of the I/Os
Mostly machine-specific, some of it is common across all games (or across a particular WPC generation)
Examples:
  - Driver #8 is connected to a flashlamp
  - Switch #10 is an opto
  - Lamp #32 is the “Shoot Again” lamp
Used by all of the layers for finer control

---
Switch Processing
All switches are polled every 2ms
At same time a “fast debounce” removes switches continuously changing from consideration
At idle time, stable switches that have changed are processed and tasks are created for each of them as necessary.
Common switch transition logic : dealing with optos, slower debouncing
Machine logic can register callback for any switch transition.

---
Lamp Processing
One lamp column is redrawn every 2ms, for a full redraw every 16ms.
Multiple “planes” can be layered for effects
Flashing APIs also provided in addition to simple on/off.