The FreeWPC
Pinball Operating System

---
FreeWPC System Architecture
Machine Logic (Rules)
Common Logic
Device
Drivers
Hardware APIs
Task APIs
Operating
System
Scheduler
Hardware
Manager
Layer
Switch
Manager
Lamp
Manager
Solenoid
Managers
Display
Manager
Hardware Interface Layer (pinio)
Hardware Definitions

---
Portability Goals
Common code across all WPC generations (WPC, WPC-DCS, WPC-S, WPC-95)
Future support for other pinball platforms (e.g. Whitestar)
Future support for new pinball hardware designs
Native compilation on PC for easier debugging
  - But not entire system can be debugged this way, some parts are replaced in native mode

---
Task Scheduler
Create new task (with optional arguments)
Query task still running
End current task
Stop different task
Sleep (minimum 16ms)
Tasks run to completion (non-preemptive)
Tasks have limited, separate stack space

---
Hardware Interface Layer
Defines how the CPU accesses the hardware
Maps simple pinball I/O operations to the correct registers & access method
Examples:
  - Set switch matrix column (N)
  - Read current switch row
  - Turn on/off solenoid (N)
Numbering of devices is machine-specific!
May require tweaking as more architectures are supported

---
Hardware Managers
Common code that uses the Hardware Interface Layer to manage devices:
  - Duty cycling of coils
  - Strobing through the switch/lamp matrix
  - Debouncing inputs
  - Real-time error detection
Each manager provides two things:
  - A real-time function that accesses the hardware
  - APIs to higher layer software
    - Example: Read Switch #N

---
WPC Hardware Managers
Switch Manager
Lamp Manager
Power Driver Managers (Continuous & Duty-Cycled, used for solenoids, motors, and flashers)
Triac Manager (Lighting & Misc. Relays)
Display (DMD) Manager
Sound Board Manager

---
Device Drivers
Works in conjunction with hardware managers for specific types of devices (e.g. ejects, slingshots, kickbacks)
Can include real-time (IRQ-level) and ordinary (task-level) functions
A single driver can refer to multiple types of hardware (e.g. a slingshot driver utilizes a coil and a switch)
Mostly written as common code that is parameterized, similar to C++ templates.

---
Common Logic
A 'library' of functions common to all pinball games
Not tied to the hardware per se
Examples:
  - Pricing, DMD drawing, Flipper Codes, Replay system, Test mode, Game state machine, Display/Lamp/Sound Effect Choreography, Enter Initials, etc.

---
Machine Logic
Machine-specific functions for rules, effects, diagnostics, etc.
Mostly event-driven, written as a series of callback functions to be invoked when certain things happen

---
Hardware Description
A set of tables that describes what hardware is connected to each of the I/Os
Mostly machine-specific, some of it is common across all games (or across a particular WPC generation)
Examples:
  - Driver #8 is connected to a flashlamp
  - Switch #10 is an opto
  - Lamp #32 is the “Shoot Again” lamp
Used by all of the layers for finer control

---
Switch Processing
All switches are polled every 2ms
At same time a “fast debounce” removes switches continuously changing from consideration
At idle time, stable switches that have changed are processed and tasks are created to handle them
Common switch transition logic : dealing with optos, slower debouncing
Machine logic can register callback for any switch transition.

---
Lamp Processing
One lamp column is redrawn every 2ms, for a full redraw every 16ms.
Multiple “planes” can be layered for effects
Flashing APIs also provided in addition to simple on/off.

---
Solenoid and Flasher Processing
Coils are handled in a variety of ways
Most coils are “pulsed”, only one at a time, with an initial high power pulse followed by a lower power pulse.
Zero-cross detection circuit is used to time the pulse for maximum bang
Flashers are similar but can run in parallel
Switched coils or continuous operation devices (e.g. motors) require separate device drivers

---
General Illumination
General lamp strings controlled through triacs
Supports on, off, and dimming states
Dimming achieved by rapidly turning on/off at precise times during the AC cycle (requires zero-cross detection)
System supports a 'default' state for each string plus it can overlay new values for a temporary lamp effect

---
Dot Matrix Processing
Display buffers are memory-mapped (any 2 of 16 at a time)
4-color mode supported via rapid page flipping
Large library of drawing functions
Transition support (wipes, fades, etc.)
128x32 full-size images can be compressed for space savings

---
WPC Hardware Registers
3FB0-3FBF : Dot matrix controller board
3FC0-3FCF : Printer/serial port/ticket dispenser
3FD0-3FDF : Sound/Fliptronics boards
3FE0-3FEF : Power Driver board, Switch Matrix
3FF0-3FFF : CPU Board internal ASIC registers

---
ASIC Functions
CPU-controllable LED (3FF2)
Fast hardware timer (3FF8) [not used]
ROM bank switching (3FFD)
Real-time clock (3FFA-3FFB)
Memory Protection (3FFD-3FFE)
Watchdog reset (3FFF)
Blanking control (3FFF)

---
Source Code Information
Approximately 36,000 lines of code (90% C, 6% Perl, 4% 6809 assembly language)
Available as GIT repository at http://github.com/bcd/freewpc
Mature and robust, development started in 2005

---
Performance
No significant degradation in performance by using C instead of assembly language
  - Key routines have been rewritten in assembler when necessary. C functions kept for portability and understandability.
Exact performance depends on the number of device drivers and realtime functions
Assembly code is inspected regularly to discover defects in the C compiler
Performance is measured regularly using a cycle-accurate 6809 simulator.

---
Dot Matrix Assembler Functions
Arbitrarily-sized bitmaps
  - Copy (used for fonts)
  - Erase
Full-size display frames
  - Copy (2.8ms)
  - Decompress (for compressed images in ROM) (varies, ~4-5ms)
  - Erase (0.5ms)
Page Operators
  - AND, OR, XOR two page buffers (1.5ms)

---
Miscellaneous Utilities Included
fontgen2 – Convert X11 fonts to FreeWPC format
gencallset – Static callback function registration
genmachine – Machine configuration compiler
srec2bin – Convert linker S-records into binary (ROM) files
wpcdebug – Debug console, requires patched pinmame
csum - ROM checksum updater/verifier

---
Miscellaneous Utilities (cont'd)
imgld – Image linker, merges image files into a single binary file
ctemp – Template compiler, used to convert templates into C code
sched – Static scheduler, generates the IRQ handler function
gendefine – Generates increasing sequence of integers by scanning source code
pgmlib – Library of PGM (image) functions
tracer – Analyze Pinmame trace files to assess performance

---
Contributions Needed
Machine configurations for more WPC games
Artists for contributing graphics/animations
Rules ideas for new games
Testers willing to install in actual machines

---
Debugging
pinmame emulator
  - With wpcdebug utility, allows printf() in 6809 code to be monitored in separate window
exec09 emulator
  - Hardware emulation not as robust but much better debugging CLI
Native mode
  - I/O accesses changed to HW emulation functions
  - Task scheduling implemented by pth library
  - 6809 functions replaced by C library equivalents (malloc, memset, etc.) except for printf()

---
Fault Detection
WPC hardware watchdog will trigger reset if not strobed every few milliseconds. Caused by a disable_interrupts() that is not released, preventing real-time function update.
Software watchdog will reset if task scheduling locks up (due to runaway task)
Blanking circuit keeps I/O disabled until software initializes successfully